## Slide 1: Ground Reference Prototype (GRP) Real Time Platform (RTP) Presentation
NEXCOM Avionics Technical Interchange Meeting (TIM)
January 30, 2003
Federal Aviation Administration (FAA)
William J. Hughes Technical Center, ACB-560
Prepared By:
CIE Engineering, Inc.
600 Maryland Avenue, SW, Suite 740
Washington, DC 20024

## Slide 2: Presentation Topics
Architecture
  GRP System Block Diagram
  GRP-RTP Functions
  GRP-RTP Architecture & Functional Flows
GRP-RTP User Information
  Connectors & Indicators
  Installation
  Operating Basics
  Maintenance & Troubleshooting

## Slide 3: GRP System Block Diagram
Real Time
Platform (RTP)
VME-Style Chassis
Ground Station - RIU
Platform (GS-RIU)
Linux-based
Laptop Computer
Multimode Digital
Radio (MDR)
ITT Transmitter
Multimode Digital
Radio (MDR)
ITT Receiver
RS-232
T1
T1
Headset w/ PTT
Ground Reference Prototype (GRP)
RF
RF

## Slide 4: GRP-RTP Functions
Interface Functions
  Front Panel Headset dual jack interface with integral PTT
  T1 Interfaces (for MDRs)
  GS-RIU RS-232 Interface
  Debug Terminal Interfaces (OTM & VCM)
Voice Functions
  Digitizes front panel headset
  ATC-10B Voice encode/decode
Messaging Functions
  GS-RIUMDR Data services (scheduled & immediate)
  RTP control services (radio control & platform configuration)
  Compressed voice message services
Timing Functions
  Generates NEXCOM timing channel
  Synchronizes all T1 interfaces to internal time base

## Slide 5: RTP Architecture
OTM
VCM
TDM Bus
RCE Audio
RCE Control
Headset
T1 MDR TX
T1 MDR RX
GS-RIU
RS-232
Debug
Debug
LEGEND:
VCM = Voice Channel Module
RCE = Radio Control Equipment
OTM = Octal T1 Module
GS-RIU = Ground Station - RIU
MDR = Multimode Digital Radio
TDM = Time Division Multiplexed
ICC = Inter-Card Communication
NEXCOM Timing Channel
PCM Audio Channel
ICC Message Channel
3.072 MHz
24 slots @ 16 bits/slot
- OTM-VCM Control
- ATC-10B Audio
TDM Master
TDM Slave
Message Routing
System Timing
Operator Voice Interface
ATC-10B Voice Processing
GRP-RTP
GRP Functionality

## Slide 6: RTP - Timing Flow
TDM Bus
RCE Audio
Headset
T1 MDR TX
T1 MDR RX
GS-RIU
The GS-RIU receives FCNT status with MDR responses or by separate request
3.072 MHz
OTM
VCM
LEGEND:
FCNT = Frame Count/NEXCOM Timing Channel
PLD = Programmable Logic Device
ICC = Inter-Card Communication
DDS = Direct Digital Synthesis
PLL = Phase Locked Loop
DDS
25 M
XTAL
PLD
ADSP-
2188M
PLL
DSP-SPORT0:
The DSP SPORT0 bus is driven at 3.072 MHz by the DDS.
The DSP generates the TDM bus frame sync at 8 kHz.
The DSP also drives the TDM FCNT channel.
8 kHz
DS21552
Framers
1.544 MHz
TDM FCNT
8 kHz
FCNT
DSP-SPORT1:
The PLL drives the 1.544 clock.
The DSP generates frame sync and the T1 FCNT channel.
AD1843
CODEC
VC-20
ATC-10B
VOCODER
3.072 MHz
ADSP-
2188M
8 kHz
TDM FCNT
8.0 kHz
9.6 kHz
VCM PLD:
The PLD provides timeslot control signals and generates 8 kHz and 9.6 kHz clocks.
CODEC:
Sample rate timing driven by 8 kHz clock.
VOCODER:
Linear and compressed interface clocks are derived from the same 3.072 MHz time base.
VCM FCNT:
The VCM timestamps all ATC-10B packets with FCNT.

## Slide 7: RTP - Typical Voice Flow
TDM Bus
MIC
T1 MDR TX
T1 MDR RX
GS-RIU
GS-RIU MESSAGES:
The GS-RIU schedules or gates CVM flow to MDR. The GS-RIU can also command the VCM to start/stop CVM flow via the OTM.
OTM
VCM
LEGEND:
TDM = Time Division Multiplexed
CVM = Compressed Voice Message
PGA = Programmable Gain Amplifier
= Linear Voice
= Compressed Voice
Message Router:
The OTM message router services all port receive queues in a round-robin fashion.
The messages are processed and forwarded, as needed, to other ports.
DS21552
Framers
FRAMER MESSAGES:
The DS21552 driver time supports scheduled and immediate message transmission.
All receive messages are time tagged with the system FCNT.
AD1843
CODEC
VC-20
ATC-10B
VOCODER
ADSP-2188M
CODEC:
The multi-channel codec supports headset and RCE audio channels.
Volume control is implemented with built-in codec PGAs.
VOCODER:
Linear and compressed interface clocks are derived from the same 3.072 MHz time base.
Mixer:
The software mixer routes linear audio.
Pre-defined configurations support signal summing.
ADSP-2188M
PHONE
Mixer
Router
ICC Channel
Message Router
& Processor
Router:
The router converts ICC messages to VC-20 nibble stream.
It supports silence packet generation.
ICC Channel:
The ICC carries CVM packets between the VCM and the OTM. Each packet contains one 96-bit data field representing 20 ms of voice.

## Slide 8: Connectors & Indicators
MDR TX
OTM Debug
MDR RX
Timing
- 1.544 MHz
- Clock Synthesizer
- Pulse A
- Pulse B
GS-RIU
Pulse Indicators
T1 Status LEDs
(16 total)
OTM Runtime LED
GS-RIU LED A
ICC RX Msg Activity
GS-RIU Rx Msg Activity
NEXCOM Epoch LED
GS-RIU LED B
ICC TX Msg Activity
GS-RIU TX Msg Activity
T1 TX LED:
- winks green for each good TX message
T1 RX LED:
- winks green for each good RX message
- winks red for each bad RX message
- solid red for carrier/frame loss conditions
OTM Front Panel

## Slide 9: Connectors & Indicators
VCM Status
ICC Message Activity
Headset Interface
RCE Control Status
RCE Control
RCE Audio
VCM Debug
VCM Front Panel

## Slide 10: VCM Headset Levels
VCM Headset Levels changed at Debug serial port
  MIC ID = 5
  HST ID = 9
Input Adjustments
  range 0 to 15decimal
Output Adjustments
  range 0 to 63decimal
Sidetone Adjustment
  range 0 to 7FFFhex
SETVOL 5 X
Xdefault= 6
ATC-10B
ENCODER
SETVOL 9 X
Xdefault= 10
ATC-10B
DECODER
STVOL X
Xdefault= 1800
SAVE CONFIG command saves
settings to FLASH
MIC
PHONE

## Slide 11: Installation
Dimensions: 19” x 11” x 16” (whd)
Power: 120 VAC, 145 W max
Connections:
  GS-RIU Port
  Headset
  MDR TX & RX
  Debug (optional for OTM/VCM)

## Slide 12: Operating Basics
  GS-RIU drives the RTP Platform
      direct user interaction is limited
  Headset:
      Press PTT to talk
      Listen for downlink audio & sidetone
  Idle LED status
      VCM Status = GREEN blinking
      OTM Runtime = GREEN blinking
  Active LED status
      VCM ICC LED = GREEN fast blinking
      OTM ICC LEDs = GREEN for each msg
      GS-RIU TX/RX LEDs = GREEN for each msg
      MDR TX/RX LEDs = GREEN for each msg

## Slide 13: Maintenance/Troubleshooting
Key resources
  LED Indications
  Debug Port
    OTM: Queue Status
    VCM: Volume & Route
  FAA GRP Design Team
Software upgrades
  XMODEM via Debug Port
  Current Release Info
    OTM = Release 6.1
    VCM = Release 6.0
Booting ... \ ************************************************** * Octal T1 Module Version 6.0 * ************************************************** SYSTEM STARTUP... ... Start Timer -> DONE ... Init QUART -> DONE ... Reset/Init DDSs/Muxes/PPs -> DONE ... Init Mque -> DONE ... Cycling LEDs -> DONE ... Init ICC -> DONE ... Start SPORT0 -> DONE ... Start SPORT1 -> DONE ... Init T1 -> DONE ... COMPLETE
POTM: VCM Status: MsgType - S MSG_SRC - 30F1: 0033 Auto_On - 30F3: 0001 Voc_Ind - 30F4: 0003 Status - 30F5: 0000 No Response from VCM Addr:30 No Response from VCM Addr:32 No Response from VCM Addr:31 Active Links: VCM Addr:33 POTM:
OTM Debug Port
Booting ... \ ************************************************ VCM Module 3
Version: X.X Built: Jan 22 2003 10:12:16
************************************************ SYSTEM STARTUP... ... Start Timer -> DONE ... Init QUART ->
... Restore System Config -> pass
Router Init Passed
... SYS_TEST Pass ... SPORT_0 Started ... CODEC Reset ... CODEC Powerup ... CODEC Standby ... CODEC Online ... 1 Vocoders Present ... SPORT_1 Started ... Debugger Started
POST Complete, Pausing: / DBG:
VCM Debug Port